The Stupidest CPU Arch Possible
(SCAP)

1:System specs
1.0:Registers by ID
BIN	HEX	NAME	Init Val
0000	0x0	A	0x00
0001	0x1	B	0x00
0010	0x2	C	0x00
0011	0x3	D	0x00
0100	0x4	E	0x00
0101	0x5	F	0x00
0110	0x6	G	0x00
0111	0x7	H	0x00
1000	0x8	I	0x00
1001	0x9	J	0x00
1010	0xA	PCH	0x00
1011	0xB	PCL	0x00
1100	0xC	SPH	0x00
1101	0xD	SPL	0xFF
1110	0xE	FLAGSH	0x00
1111	0xF	FLAGSL	0x00

1.1:Instructions by CLASS
CLASS(BIN)	CLASS(HEX)	Name	Bytes used
0000	0x0	LD/LDI/ST/MV/SWP	ALL
0001	0x1	ADD/SUB/ADDS/SUBS	2
0010	0x2	SL/SR/ROL/ROR/AND/OR/XOR	2
0011	0x3	PUSH/POP	2
0100	0x4	TESTU/TESTS	2,3
0101	0x5	JMP/CNDJMP	2-3
0110	0x6	CALL/RET	2-3
0111	0x7	-	-
1000	0x8	-	-
1001	0x9	-	-
1010	0xA	-	-
1011	0xB	-	-
1100	0xC	-	-
1101	0xD	-	-
1110	0xE	-	-
1111	0xF	NOP	-

1.3:Pipeline
Number	Name	Purpuse	Optional
1.	Fetch	Fetch 1st byte	NO
2.	Decode	Decode 1st byte and Fetch the 2nd	NO
3.	Execute 1	if 3 bytes are enough, Fetch 3rd byte and Execute	NO
4.	Execute 2	ONLY if 3 bytes are not enough, Fetch the 4th byte and execute	YES
5.	WriteBack	Write data back if needed and increment PC by 4 if class ID is not 0x5	NO

2:Address space
Borders	Name	Nature
0x0000-0x00FE	Bootrom	ROM
0x00FF-0xFEFF	General Pourpuse	Fuckin’ anything
0xFF00-0xFFFD	Device Range	MMIO
0xFFFE-0xFFFF	Interupt Address	MMIO

3:Instruction format
CLASS ID	2nd Byte	3rd Byte	4th Byte
0x0	REG1,REG2	ADDRL / IMM	ADDRH / -
0x1	REG1,REG2	-	-
0x2	REG1,REG2	-	-
0x3	REG1,REG2	-	-
0x4	REG1,REG2	TESTTYPE	-
0x5	ADDRL / -	ADDRH / -	-
0x6	ADDRL / -	ADDRH / -	-
0x7	-	-	-
0x8	-	-	-
0x9	-	-	-
0xA	-	-	-
0xB	-	-	-
0xC	-	-	-
0xD	-	-	-
0xE	-	-	-
0xF	-	-	-

4:Interrupts
When the interrupt line is pulsed, the CPU jumps to the address whose lower byte is the byte read from 0xFFFE and upper one is the byte read from 0xFFFF. Interrupts behave like CALL instructions. An interrupt takes 4 clock cycles(2 to write the PC to stack,2 to read the new location)